## Slide 1: Optimized, Bottom-Up Semantic Web Reasoning based on OWL2 RL in Resource-Constrained Settings
William Van Woensel

## Slide 2: Context
Clinical Practice Guidelines (CPG)
  Disease-specific, evidence-based recommendations
  Standard for decision making on diagnosis, prognosis and treatment
  Context-sensitive care recommendations
  Clinical workflow of relevant clinical activities
Algorithm for diagnosis of heart failure [1]
Pre-treatment assessment and
correction of electrolytes [2]
ACEI upitration [3]

## Slide 3: Context (2)
Clinical Decision Support Systems (CDSS)
  Automated systems that incorporate computerized CPG
  Pro-actively guide physician through decision processes
Decision Logic (OWL2 DL), IF-THEN (SWRL) rules, .. Canadian Community Health Survey (2014):
    Chronic illnesses affect ca. 40% of Canadians
    With multi-morbidity of ca. 15%
  Increase self-sufficiency and quality of life
  Reduce healthcare costs
Mobile patient diaries
  Self-collect health data at any time and place
    Using Bluetooth measurement devices (e.g., IBGStar, OneTouch, Withings, iHealth)
  Increase mobility of chronic patients
  Up-to-date health profile
  No delays in supplying health-critical info
Class hierarchy of CPG-DKO [2]
…
Switch [2]:

## Slide 4: Context (2)
Clinical Decision Support Systems (CDSS)
  Automated systems that incorporate computerized CPG
  Pro-actively guide physician through decision processes
Involve patients in their own long-term care
  Canadian Community Health Survey (2014):
    Chronic illnesses affect ca. 40% of Canadians
    With multi-morbidity of ca. 15%
  Increase self-sufficiency and quality of life
  Reduce healthcare costs
Mobile patient diaries
  IMPACT-AF project
  Self-collect health data at any time and place
    Using Bluetooth measurement devices (e.g., IBGStar, OneTouch, Withings, iHealth)
  Increase mobility of chronic patients
  Up-to-date health profile
  No delays in supplying health-critical info

## Slide 5: Context (3)
Requirements:
  Connectivity
    Cope with short/long-term disconnections (lack of WiFi, 3G)
    Should not limit mobile patient diary usage
  Response latency
    Slow / lacking connectivity may occur frequently
    Server = single point of failure
Solutions:
  Offline data entry (BP, HR, ..)
    Synchronize with online EMR when connectivity is restored
  Local Clinical Decision Support System
    Independent of connectivity
    Enables timely health alerts
  Distributed setup
    Local: lightweight, time-sensitive reasoning is deployed locally
    Remote: heavyweight processes are delegated to the server

## Slide 6: Context (4)
Ontology-based (OWL) reasoning
  OWL2 DL: too resource-intensive on mobile systems
  Recent empirical work by Bobed et al. [3]:
    PC outperforms Android by 1,5 – 150
    Larger number of out-of-memory errors
  Most mobile approaches are rule-based
    E.g., OWL2 RL or custom entailment
OWL2 RL
  Suitable W3C OWL2 profile
    Allows scalable reasoning without sacrificing too much expressivity
  Adjust reasoning complexity to suit scenario & resources
    Choose rule subsets based on task & overhead
  Enhance any rule-based task with semantic features
    I.e., include OWL2 RL (subset) into ruleset
  Such as computerized, rule-based CPG in CDSS
Notes: Galaxy Nexus (Android 4.2.1, 1.2 GHz dualcore, 1 GB RAM, released in 2011, in the following denoted as A1)
Galaxy 655 Tab 2 7.0 (Android 4.1.2, 1 GHz dual-core, 1 GB RAM, released in 2012, denoted A2)

## Slide 7: 1) Optimizing the OWL2 RL ruleset
Multi-stage OWL2 RL ruleset selection
  Stable vs. volatile ontology
  Conformant
Equivalent OWL2 RL ruleset
  Removing logically equivalent rules
  Replace 2+ specific rules with more general rules & axioms
  Removing “stand-alone” schema inference rules
Purpose- and reference-based subsets
  Purpose: inferencing vs. validation
  Reference: instances vs. schema
Remove inefficient rules
  Leave out rules with large performance impact
    E.g., #eq-ref infers each resource is equivalent to itself
Domain-based ruleset selection
  I.e., leave out rules not needed by ontology & dataset
  Forward-chaining algorithm (Tai et al. [7])
Stable
Non-conformant
Notes: Removing logically equivalent rules: i.e., rules of which the results are covered by other rule(s)
Some of these break conformance with OWL2 RL axiomatization:

## Slide 8: 1) Optimizing the OWL2 RL ruleset: evaluation
Notes: Conformant – Volatile : ca. 94% (-6%)
Conformant – Stable (inf-inst): ca. 44% (-56%)
Non-conformant – Volatile: ca. 55% (-45%)
Non-conformant – Stable (inf-inst): ca. 10% (-90%)

## Slide 9: 1) Optimizing the OWL2 RL ruleset: future work
Rule instantiation [6, 8, 9]
  Materialize schema inferences in ontology
  Instantiate each instance rule with schema terms
    Increase rule selectivity
    Reduce # of joins
  Requires a “stable” ontology
Domain-specific rulesets
  Currently, does not support “volatile” ontologies
    Ruleset needs to be re-calculated on ontology changes
    Avg. ca. 291ms (PC), 4183ms (mobile)
  Deploy on mobile device, integrate with reasoner

## Slide 10: 2) RETE Strategies for Resource-Constrained Settings
RETE Algorithm
  Well-known solution to implement production rule systems
  Rule premise = alpha node
    Alpha memory: keeps matched facts
  Join = beta node
    Beta memory: keeps join results
  Useful in dynamic environments, due to its incremental nature
Known for trading memory for performance
  Alpha memories will overlap depending on premise selectivity
  Many SW applications already involve an RDF store for query access
    Collection of alpha memories duplicate RDF store
Many rules will not be needed for domain
  But, still consume computing & memory resources in RETE
  Tailor RETE networks during execution
    In light of dynamic & incremental situations

## Slide 11: 2) RETE Strategies for Resource-Constrained Settings (2)
Dataset-mask memory strategy
  Keep alpha memories as masks on the RDF store
  Query RDF store using joining token & rule premise as constraint
  Hybrid version: dataset-mask vs. regular memory, based on premise selectivity
Dynamic tailoring of RETE networks
  Avoid redundant join attempts [10]
    Unlink alpha memory from its beta node in case join attempts are useless
  Avoid redundant token matches
    Pause alpha nodes in case they are unlinked from each rule
    Requires separate RDF store for synchronizing alpha memory upon resume
  Join-utility heuristics
    Determine utility of join attempts
  Empty sibling memory
    In case alpha (i <= 2) or beta (i > 2) memory is empty, no joins are possible [10]
  Lower failed alpha nodes
    Pointless to attempt joins in case a failed alpha node occurs lower down
Notes: Pause alpha nodes: assumes that standard-practice optimizations, such as re-using alpha nodes, are applied
(Heuristics: avoid false negatives (i.e., join attempts were indeed useful))

## Slide 12: 2) Dynamic tailoring of RETE networks
Responsiveness to Incremental Reasoning Scenarios
Notes: The rule failed at time t0
Both join-utility heuristics hold for non-failed alpha nodes α1 and α3: i.e., their sibling memories are empty, and a lower-down alpha node (node α4) has failed
As a result, their memories were unlinked from the related beta nodes. Further, the α3 node memory is paused, since it is unlinked from each related rule.
Triggers (?i) are installed that listen for when the applicable heuristics no longer hold.
At time , a new token A4 matches node α4 (satisfying heuristic (2))
At time , an incoming token A2 is matched to the previously failed node α2 (satisfying heuristic (1)).
So, trigger ?1 will be activated at time , re-linking the α1 memory to beta node β1. This results in the joined token A12 activating the ?2 trigger, since the sibling memory of α3 is no longer empty, similarly re-linking the memory, and resuming node α3 (since it is now become relevant again)
Finally, this results in a complete inference A1234 for the rule.
The rule failed at time t0
Both join-utility heuristics hold for non-failed alpha nodes α1 and α3: i.e., their sibling memories are empty, and a lower-down alpha node (node α4) has failed
As a result, their memories were unlinked from the related beta nodes. Further, the α3 node memory is paused, since it is unlinked from each related rule.
Triggers (?i) are installed that listen for when the applicable heuristics no longer hold.
At time 𝑡_𝑥, a new token A4 matches node α4 (satisfying heuristic (2))
At time 𝑡_𝑦, an incoming token A2 is matched to the previously failed node α2 (satisfying heuristic (1)).
So, trigger ?1 will be activated at time 𝑡_𝑦, re-linking the α1 memory to beta node β1. This results in the joined token A12 activating the ?2 trigger, since the sibling memory of α3 is no longer empty, similarly re-linking the memory, and resuming node α3 (since it is now become relevant again)
Finally, this results in a complete inference A1234 for the rule.

## Slide 13: Dataset-mask: evaluation (1)
Notes: Memory savings for dataset-mask are tremendous: only 0,05% of tokens are needed
(each dataset-mask memory keeps a mask that counts as a token)
But, reasoning times are significantly increased, by factors of avg. ca. 3,3 and 2,8 for PC and mobile
(note that performance times for PC and mobile are not directly comparable, since, as mobile benchmarks are executed on a subset of the PC ontologies)

## Slide 14: Dataset-mask: evaluation (2)
What if SW scenario does not include an RDF store?
  Introduce RDF store as shared alpha memory pool
Updated memory reductions:
  Dataset-mask: avg. ca. -55%
  Hybrid-0.1,0.25: avg. ca. -27%
  Hybrid-0.5: avg. ca. -9%
  Hybrid-0.75,1: avg. ca. +1%
RDF store update operations:
  PC: avg. ca. +0,67s
  Mobile: avg. ca. +1s

## Slide 15: Dynamic RETE tailoring: evaluation
Notes: large majority of unlinking operations is due to heuristic (1), i.e., empty sibling memory
(upon closer inspection, the premise “?x ?p ?x” only occurs in unsuccessful OWL2 RL rules for each ontology
so, its related alpha node is unlinked from each rule and paused each time
a second node “?y rdf:type ?ci” was paused twice, and resumed twice.)
overhead of individual tailoring operations is negligible, with the collective overhead (i.e., total time) not exceeding 50ms on PC and 80ms on mobile
RETE operation statistics column indicates the impact of dynamic tailoring on the number of RETE operations
(regarding the alpha node for premise “?x ?p ?x”, the system will attempt to match every single incoming token to it)
by pausing this node for each ontology (and twice another node) ..)
the number of attempted token matches is decreased by avg. ca. -17% (-36351 operations)
the number of join attempts is greatly decreased, by avg. ca. -68% (-1405345 operations)
a priori network tailoring further decreases the number of RETE operations:
avg. ca. -39% (-85207 operations) for attempted token matches
avg. ca -86% (!) (-1782423 operations) for join attempts
however, this comes at the expense of losing reasoning completeness when faced with incremental scenarios
also, it requires a naïve reasoning algorithm to be performed beforehand, which also yields a non-trivial overhead (preproc column)
reasoning times column shows the overall performance for initial (initial dataset column) and subsequent (incremental column) reasoning cycles
performance impact is much higher on the mobile platform than on PC, reflecting the reduced processing capabilities.
in fact, performance improvements on PC are virtually negligible
dynamic tailoring in incremental reasoning optimizes performance by avg. ca. -76ms (-0.5%) on PC and -2,9s (-12,3%) on mobile.
a priori tailoring in incremental reasoning reduces reasoning times by avg. ca. -172ms (1,2%) on PC and -4,2s (-17,9%) on mobile
but, requires a non-trivial pre-processing step (especially on mobile)
if we don’t include the pre-processing step, a priori tailoring thus yields the highest increase in performance, but at the expense of reasoning completeness
we observed that this strategy resulted in loss of a total of 11448 inferences for 5 ontologies
further, its pre-processing step involves a one-time overhead that is non-trivial on PC (avg. ca. 291ms) and a quite large overhead on mobile (avg. ca. 4,2s)
this strategy seems mostly useful for non-incremental reasoning on a series of similar datasets, each utilizing similar terms and data patterns
whereas dynamic tailoring deals with arbitrary incremental scenarios, guaranteeing reasoning completeness

## Slide 16: Future work (in progress)
Currently: mostly based on OWL2 RL ruleset in clinical decision support
  Also, benchmarks done using OWL2 RL ruleset
  Additional benchmarks needed for other rulesets
More advanced heuristics to determine join utility
  Eager vs. lazy algorithm
More fine-grained memory strategy
  Alpha memories will often subsume other memories
  E.g., subsumed (virtual) alpha memories access their subsuming, concrete alpha memory behind-the-scenes (comparable to dataset-mask but with a smaller query access overhead)
Dynamic hybrid memory strategies
  Switch between regular and dataset-mask memories based on evolving selectivities
.. virtual materialization of OWL2 semantics in join operations
Notes: OWL2 RL ruleset: some of its rules including overly general wildcard premises (i.e., “?x ?p ?y”)
for other rulesets with more concrete premises, utilizing dataset-mask memories will likely lead to smaller memory reductions
also, seeing how overly general rule premises match many more tokens, memory unlinking and node pausing will also have a smaller performance impact

## Slide 17: References
[1] S. Abidi. PhD Thesis, 2010.
[2] B. Jafarpour. PhD Thesis, 2010.
[3] C. Bobed, R. Yus, F. Bobillo, E. Mena. Semantic reasoning on mobile devices: Do androids dream of efficient reasoners? Web Semantics: Science, Services and Agents on the World Wide Web, 35:167–183, December 2015.
[4] S. Ali and S. Kiefer. “microOR --- A Micro OWL DL Reasoner for Ambient Intelligent Devices. In Proceedings of the 4th International Conference on Advances in Grid and Pervasive Computing, 2009, pp. 305–316.
[5] T. Kim, I. Park, S. J. Hyun, D. Lee. MiRE4OWL: Mobile Rule Engine for OWL. In Proceedings of the 2010 IEEE 34th Annual Computer Software and Applications Conference Workshops, 2010, pp. 317–322.
[6] B. Motik, I. Horrocks, S. M. Kim. Delta-reasoner: A Semantic Web Reasoner for an Intelligent Mobile Platform. In Proceedings of the 21st International Conference Companion on World Wide Web, 2012, pp. 63–72.
[7] W. Tai, J. Keeney, D. O’Sullivan. Resource-constrained reasoning using a reasoner composition approach. Semant. Web, vol. 6, no. 1, pp. 35–59, 2015.
[8] J. Bak, M. Nowak, C. Jedrzejek. RuQAR: Reasoning Framework for OWL 2 RL Ontologies. In The Semantic Web: ESWC 2014 Satellite Events, Anissaras, Crete, Greece, May 25-29, 2014, 2014, vol. 8798, pp. 195–198.
[9] G. Meditskos N. Bassiliades. DLEJena: A Practical Forward-chaining OWL 2 RL Reasoner Combining Jena and Pellet. Web Semant., vol. 8, no. 1, pp. 89–94, Mar. 2010.
[10] R.B. Doorenbos. Combining Left and Right Unlinking for Matching a Large Number of Learned Rules. In Hayes-Roth, B. and Korf, R.E. (eds.) Proceedings of the 12th National Conference on Artificial Intelligence, Seattle, WA, USA, July 31 - August 4, 1994, Volume 1. pp. 451–458. {AAAI} Press / The {MIT} Press (1994).